Last Charge Design

The Last Charger You’ll Ever Need

# Design Goals
## Must haves:
- Measure cell current to within 1mA in the range 0 to 50mA and within 10mA within the range 100mA to4A
- Measure cell voltage to within 1mV in the range 0.5V to 2V
- Control charge current to within 5mA in range 0-50mA, 50mA in range 100mA to 4A
- Ability to trickle charge at 0.01C
- Fast charge at 1C (up to 3A @ 1.5V)
- Fast charge termination using -dv/dt method
- Display to view charge statistics
- Modular design with 1 cell per module
- Modules for AA and AAA cells
- Cell discharge at approximately 1A
- Powered from a 12V barrel jack
- Programming port
- Three button UI
## Nice to haves:
- Measure cell temperature
- Fast charge termination using dT/dt termination
- Powered from USBC PD
- Cell insertion detection
- 4 wire voltage sense

## User Interface
The UI shall consist of three push buttons for Up, Down and Enter respectively. These buttons will be used to navigate a menu that is displayed on a graphical OLED display. The display should update at least once per second, and show battery voltage, current, charge state as well as allow selecting battery capacity before charging and choosing operating mode (STANDBY, CHARGE, CYCLE)

Display options
- PIM473 128x128 white OLED
  - https://core-electronics.com.au/1-12-mono-oled-128x128-white-black-breakout.html
- MDOG128128FV-WM 128x128 white OLED
  - https://au.element14.com/midas/mdog128128fv-wm/display-128-x-128-cog-wht-on-blk/dp/4048487?CMP=GRHB-OCTOPART
## Power

## Microcontroller

## Charge
### Potential Components
MPN	Manufacturer	Description
MAX1640	Analog Devices	Adjustable-Output, Switch-Mode Current Sources with Synchronous Rectifier
INA293	TI	-4-V to 110-V, 1.3-MHz, ultra-precise current sense amplifier
MCP3426	Microchip	16-Bit, Multi-Channel ΔΣ Analog-to-Digital Converter with I2C™ Interface and On-Board Reference
MCP4726	Microchip	12-Bit Single Output DAC w/EEPROM and I2C™

### Resources
Description	Link
Voltage- and Current-Mode Control for PWM Signal Generation in DC-to-DC Switching Regulators	https://www.digikey.com.au/en/articles/voltage-and-current-mode-control-for-pwm-signal-generation-in-dc-to-dc-switching-regulators
Using PFM to Improve Switching DC/DC Regulator Efficiency at Low Loads	https://www.digikey.com.au/en/articles/using-pfm-to-improve-switching-dc-dc-regulator-efficiency-at-low-loads
Simple Solutions for a Single-Device Pulse-Width Modulation (PWM) Waveform Generator	https://www.analog.com/en/technical-articles/simple-solutions-for-a-singledevice-pulsewidth-modulation-pwm-waveform-generator.html
HOW TO BUILD A SAWTOOTH AND TRIANGLE WAVE GENERATOR	https://www.circuitbasics.com/what-are-sawtooth-and-triangle-wave-generators/

### Control
Current control requirement is 5mA between 0 and 50mA and 50mA between 100mA and 4A, 12 bit DAC should be sufficient for this. I2C would be optimal.

### Measurement
For current measurement requirement 1mA from 0 to 4A we need 12 bits ADC, choose 16 bit ADC to be safe. Will need high side current sense resistor and current sense differential amplifier to take this measurement. The amplified signal may be fed back to control loop.
For voltage measurement requirement 1mV from 0.5 to 2V need 11 bit ADC, for margin and BOM choose 16 bit ADC same as current measurement. Voltage buffer needed, using opamp.
I2C ADCs would be optimal for these.
Block Diagram