Last Charge Design

The Last Charger You’ll Ever Need

# Design Goals
## Must haves:
- Measure cell current to within 1mA in the range 0 to 50mA and within 10mA within the range 100mA to4A
- Measure cell voltage to within 1mV in the range 0.5V to 2V
- Control charge current to within 5mA in range 0-50mA, 50mA in range 100mA to 4A
- Ability to trickle charge at 0.01C
- Fast charge at 1C (up to 3A @ 1.5V)
- Fast charge termination using -dv/dt method
- Display to view charge statistics
- Modular design with 1 cell per module
- Modules for AA and AAA cells
- Cell discharge at approximately 1A
- Powered from a 12V barrel jack
- Programming port
- Three button UI
## Nice to haves:
- Measure cell temperature
- Fast charge termination using dT/dt termination
- Powered from USBC PD
- Cell insertion detection
- 4 wire voltage sense

## User Interface
The UI shall consist of three push buttons for Up, Down and Enter respectively. These buttons will be used to navigate a menu that is displayed on a graphical OLED display. The display should update at least once per second, and show battery voltage, current, charge state as well as allow selecting battery capacity before charging and choosing operating mode (STANDBY, CHARGE, CYCLE)

Display options
- PIM473 128x128 white OLED
  - https://core-electronics.com.au/1-12-mono-oled-128x128-white-black-breakout.html
- MDOG128128FV-WM 128x128 white OLED
  - https://au.element14.com/midas/mdog128128fv-wm/display-128-x-128-cog-wht-on-blk/dp/4048487?CMP=GRHB-OCTOPART
## Power

## Microcontroller

## Charge
### Potential Components
MPN	Manufacturer	Description
MAX1640	Analog Devices	Adjustable-Output, Switch-Mode Current Sources with Synchronous Rectifier
INA293	TI	-4-V to 110-V, 1.3-MHz, ultra-precise current sense amplifier
MCP3426	Microchip	16-Bit, Multi-Channel ΔΣ Analog-to-Digital Converter with I2C™ Interface and On-Board Reference
MCP4726	Microchip	12-Bit Single Output DAC w/EEPROM and I2C™
TLC555	Texas Instruments	555 Type, Timer/Oscillator (Single) IC 2.1MHz 8-SOIC

### Resources
Description	Link
Voltage- and Current-Mode Control for PWM Signal Generation in DC-to-DC Switching Regulators	https://www.digikey.com.au/en/articles/voltage-and-current-mode-control-for-pwm-signal-generation-in-dc-to-dc-switching-regulators
Using PFM to Improve Switching DC/DC Regulator Efficiency at Low Loads	https://www.digikey.com.au/en/articles/using-pfm-to-improve-switching-dc-dc-regulator-efficiency-at-low-loads
Simple Solutions for a Single-Device Pulse-Width Modulation (PWM) Waveform Generator	https://www.analog.com/en/technical-articles/simple-solutions-for-a-singledevice-pulsewidth-modulation-pwm-waveform-generator.html
HOW TO BUILD A SAWTOOTH AND TRIANGLE WAVE GENERATOR	https://www.circuitbasics.com/what-are-sawtooth-and-triangle-wave-generators/

### Control
Current control requirement is 5mA between 0 and 50mA and 50mA between 100mA and 4A, 12 bit DAC should be sufficient for this. I2C would be optimal.

### Measurement
For current measurement requirement 1mA from 0 to 4A we need 12 bits ADC, choose 16 bit ADC to be safe. Will need high side current sense resistor and current sense differential amplifier to take this measurement. The amplified signal may be fed back to control loop.
For voltage measurement requirement 1mV from 0.5 to 2V need 11 bit ADC, for margin and BOM choose 16 bit ADC same as current measurement. Voltage buffer needed, using opamp.
I2C ADCs would be optimal for these.

### Buck Converter
One of the secondary goals of this project was for me to gain a better understanding of how DC to DC converters work. I felt this was a good opportunity to learn as the load is fairly constant, however being constant current rather than constant voltage did mean that a few things had to be changed compared to online resources for constant voltage supplies. This goal drove me to minimise the use of complex integrated circuits, the whole converter is mostly transistors, opamps and passive components with a couple of notable exceptions. Hopefully by reading this document and studying the circuits you will be able to get a much better understand of buck converters as well.
A buck converter has three main parts, PWM generator, power stage and feedback stage. The PWM generator creates the control signal for driving the power stage. The higher the duty cycle of the PWM, the higher the output voltage. For an ideal buck converter this relationship is:
V_{ out } = D times V_{ "in" }
which can be found using simple relationships for inductors and capacitors. The power stage contains switching elements (usually N channel mosfets), inductive and capacitive elements to convert the input voltage to a lower output voltage. Finally the feedback stage produces an error signal from the output compared to a reference which is used to control the PWM duty cycle.
#### PWM Generator
The PWM generator in each Last Charge module uses a 555 timer IC to generate a square wave output at 100KHz, the switching frequency of the converter. This signal is used to charge and discharge a capacitor with a constant current, to produce a triangular wave between 1/3 and 2/3 of the supply voltage. The triangle wave is buffered then dropped down to a 0-5V range using a voltage divider, before a comparator compares it to a control signal. The amount of time that the triangle wave is above the control signal determines the duty cycle. The comparator and buffer need to be appropriately fast to create fast edges for driving the power stage, which helps to minimise power losses.
#### Power Stage
Synchronous converters
Gate drivers, bootstrap capacitor
Continuous conduction vs discontinuous conduction mode
Block Diagram