Last Charge Design

The Last Charger You’ll Ever Need

# Design Goals
## Must haves:
- Measure cell current to within 1mA in the range 0 to 50mA and within 10mA within the range 100mA to4A
- Measure cell voltage to within 1mV in the range 0.5V to 2V
- Ability to trickle charge at 0.01C
- Fast charge at 1C (up to 3A @ 1.5V)
- Fast charge termination using -dv/dt method
- Display to view charge statistics
- Modular design with 1 cell per module
- Modules for AA and AAA cells
- Cell discharge at approximately 1A
- Powered from a 12V barrel jack
- Programming port
- Three button UI
## Nice to haves:
- Measure cell temperature
- Fast charge termination using dT/dt termination
- Powered from USBC PD
- Cell insertion detection
- 4 wire voltage sense

## User Interface
The UI shall consist of three push buttons for Up, Down and Enter respectively. These buttons will be used to navigate a menu that is displayed on a graphical OLED display. The display should update at least once per second, and show battery voltage, current, charge state as well as allow selecting battery capacity before charging and choosing operating mode (STANDBY, CHARGE, CYCLE)

## Power

## Miocrocontroller

## Charge
### Potential Components
MPN	Manufacturer	Description
MAX1640	Analog Devices	Adjustable-Output, Switch-Mode Current Sources with Synchronous Rectifier

### Resources
Description	Link
Voltage- and Current-Mode Control for PWM Signal Generation in DC-to-DC Switching Regulators	https://www.digikey.com.au/en/articles/voltage-and-current-mode-control-for-pwm-signal-generation-in-dc-to-dc-switching-regulators
Using PFM to Improve Switching DC/DC Regulator Efficiency at Low Loads	https://www.digikey.com.au/en/articles/using-pfm-to-improve-switching-dc-dc-regulator-efficiency-at-low-loads
Simple Solutions for a Single-Device Pulse-Width Modulation (PWM) Waveform Generator	https://www.analog.com/en/technical-articles/simple-solutions-for-a-singledevice-pulsewidth-modulation-pwm-waveform-generator.html
HOW TO BUILD A SAWTOOTH AND TRIANGLE WAVE GENERATOR	https://www.circuitbasics.com/what-are-sawtooth-and-triangle-wave-generators/

Block Diagram